## Slide 1
Personalized Femoral Implant Planning by Automatic Femur Segmentation
Iwan Paolucci, Severin Tobler
University of Bern
16. December 2015, Medical Image Analysis Lab

## Slide 2: Introduction
Goal: DICE 0.95 with 0.05 std

## Slide 3: Methods – Algorithm Pipeline
Tree Model
MR Data
Pre-Process
Feature Extraction
Random Forest
Post-Process
Segmented Volume

## Slide 4: Methods – Pre-Process
Normalization
Noise removal
  3D Wiener filter

## Slide 5: Methods – Feature Extraction
Relative position (3D)
Standard deviation
Entropy
Gaussian
Average
Laplacian of Gaussian
Laplacian
Prewitt (horizontal and vertical)
Sobel (horizontal and vertical)
Notes: Total 13 features
Filters are applied on 2D slides
Random Forest

## Slide 6: Methods – Post-Processing
Morphological opening
Keep largest area / volume
Fill holes
Notes: Opening: erosion, dilatation
Improvement in every case
No thresholding (0.5)

## Slide 7: Results
DICE 0.91 with 0.03 std
DICE 0.86 with 0.04 std
Notes: RF: num: 20, max: 0.9283, min: 0.7770, mean: 0.8603, median: 0.8573, range: 0.1513, std: 0.0432
PP: num: 20, max: 0.9590, min: 0.8495, mean: 0.9108, median: 0.9002, range: 0.1094, std: 0.0313
5 fold cross validation

## Slide 8: Discussion
Objective best and worst case:
Notes: Dice interpretation: DICE 0.91 with 0.03 std; goal: 0.95 with 0.05 std
Slim & Fast, performs on a commercial laptop (5MB (tree model), computation time 2.5 min (whole segmentation))
Segmentation is always the Femur
Front part of the bone is still ‘good’ => femoral implant
Mean: 2.5 min +- 0.5 min
Core 2 duo 1.8 GHz, 6 MB L2 Cash, 4 GB RAM

## Slide 9: Outlook
Include prior information
Investigate 3D features
Extend to further bone structure
Notes: Prior information: eg include gender/age/weight/height, ASM

## Slide 10: Thanks for your attention!
Questions?

## Slide 11: Results Cross Validation (5 fold)

## Slide 12: Random Forest
15 Trees
Leaf size of 1
Trained on 15 volumes
1% Sample proportion
13 Features
~ 5 MB